## Slide 1
SSE & AVX
System Programming Laboratory · SSE / AVX in assembly
1 / 37

## Slide 2
Foundations & scalar
The register model, how to read the instructions, and how to call libc from assembly — then three single-lane programs.
System Programming Laboratory · SSE / AVX in assembly
3 / 37

## Slide 3
FOUNDATION · A SHORT HISTORY
SSE and AVX through the years
Each generation widened the registers or added instructions — and stayed backward-compatible.
1999
SSE
128-bit xmm · floats
2001
SSE2
+ doubles, integers
2004
SSE3
horizontal math
2006
SSSE3
shuffles, bytes
2007–08
SSE4
.1 + .2: dot-product, strings
2011
AVX
256-bit ymm · VEX · 3-operand
2013
AVX2 + FMA
256-bit integer · fused mul-add
2016–17
AVX-512
512-bit zmm · EVEX · 32 regs · masks
SSE era — 128-bit
AVX era — 256 → 512-bit
System Programming Laboratory · SSE / AVX in assembly
5 / 38

## Slide 4
FOUNDATION · THE REGISTERS
The vector register file: xmm ⊂ ymm ⊂ zmm
zmm (512-bit)
ymm (256-bit)
xmm (128-bit)
bit 0
127
255
511
Nested, low bits first
SSE gave 128-bit xmm0..15; AVX widened them to 256-bit ymm; AVX-512 to 512-bit zmm. Each lives in the low bits of the next. A write through a v-prefixed (AVX) instruction zeroes the unused upper bits.
Lanes — how many fit
Each register is a row of independent slots called lanes (נתיב). A float is 32 bits, a double 64. So: xmm = 4 floats / 2 doubles · ymm = 8 / 4 · zmm = 16 / 8.
System Programming Laboratory · SSE / AVX in assembly
4 / 37

## Slide 5
FOUNDATION · READING THE NAMES
Decode a mnemonic in four parts
Once you can read the name, the base instruction set is systematic. Read it left to right:
[ v ]
optional AVX / VEX prefix — wider regs, 3-operand form
op
the operation: add · sub · mul · div · sqrt · max · mov
{ s | p }
scalar — one lane · packed — every lane
{ s | d }
single-precision (float) · double-precision
SSE (no prefix, 128-bit)
AVX (v…, 128/256-bit)
decodes as
addss
vaddss
add · scalar · single
addps
vaddps
add · packed · single
mulpd
vmulpd
mul · packed · double
sqrtss
vsqrtss
sqrt · scalar · single
maxps
vmaxps
max · packed · single
The v prefix
addps and vaddps decode to the SAME operation — add · packed · single. The v selects the AVX encoding (3-operand form, optional 256-bit ymm). Drop the v and you have the SSE instruction.
The difference between SSE and AVX ops on xmm is whether or not we clear out the upper 128-bit of ymm
System Programming Laboratory · SSE / AVX in assembly
5 / 37

## Slide 6
FOUNDATION · NO C — CALL LIBC DIRECTLY
The floating-point ABI (System V AMD64)
arguments
first 8 float/double args → xmm0 … xmm7
return
float/double result → xmm0
caller-saved
any call may clobber every xmm — save what you need
calling printf from assembly
; the shape of every printf call we make
extern printf
; ... compute a float result in xmm0 ...
cvtss2sd xmm0, xmm0 ; float -> double for %f
lea rdi, [rel fmt] ; "= %f\n"
mov eax, 1 ; AL = # vector regs used
call printf wrt ..plt ; external call via PLT
; three rules to get this right:
; 1) AL = number of xmm args (0 if none)
; 2) rsp 16-byte aligned at the call
; 3) widen float->double for %f
System Programming Laboratory · SSE / AVX in assembly
6 / 37
RIP-relative data
[rel fmt] addresses the string as a signed 32-bit offset from RIP — not an absolute address. That is what makes the program position-independent under default gcc.

## Slide 7
FOUNDATION · THE THREE RULES
Why a printf call needs this setup
1 · The AL convention
printf is variadic. For a variadic call, AL holds how many xmm registers carry arguments. Printing one float → mov eax, 1. Strings/ints only → xor eax, eax.
2 · Stack alignment
rsp must be 16-byte aligned at the call instruction. The prologue push rbp / mov rbp,rsp / and rsp,-16 guarantees it.
3 · float vs double
%f prints a double. In C, a float argument is auto-promoted to double for you. In asm there is no compiler — you widen it yourself with cvtss2sd.
Why call printf wrt ..plt?
We go through the PLT (Procedure Linkage Table) so the program works as position-independent code
System Programming Laboratory · SSE / AVX in assembly
7 / 37

## Slide 8
PROGRAM 1 · CPUID.ASM
Detecting features with one instruction
How cpuid works
Put a leaf number in EAX, run cpuid, and the CPU writes feature bits into EAX/EBX/ECX/EDX. One bit per feature.
leaf 1 → EDX[25]=SSE EDX[26]=SSE2
leaf 1 → ECX[28]=AVX ECX[12]=FMA
leaf 7 → EBX[5]=AVX2 EBX[16]=AVX-512F
cpuid clobbers all four GP registers — so we save the words to memory, then test bits.
cpuid.asm — gather words, then test bits
mov eax, 1
cpuid ; -> EDX, ECX feature words
mov [edx1], edx ; stash before they're lost
mov [ecx1], ecx
mov eax, 7
xor ecx, ecx ; sub-leaf 0 (required)
cpuid ; -> EBX (AVX2 = bit 5)
; test one bit: shift down, mask 1
mov eax, [ecx1]
shr eax, 28 ; AVX is ECX bit 28
and eax, 1 ; -> 0 or 1
System Programming Laboratory · SSE / AVX in assembly
8 / 37

## Slide 9
System Programming Laboratory · SSE / AVX in assembly
9 / 37

## Slide 10
PROGRAM 1 · CPUID.ASM — RUN IT
shell
# build just this one
nasm -f elf64 cpuid.asm -o cpuid.o
gcc cpuid.o -o cpuid
./cpuid
output
$ ./cpuid
SIMD support (read straight from CPUID):
sse : yes
sse2 : yes
avx : yes
fma : yes
avx2 : yes
avx512f : no
System Programming Laboratory · SSE / AVX in assembly
9 / 37

## Slide 11
PROGRAM 1 · DEBUGGING
build with debug info (-g -F dwarf)
nasm -f elf64 -g -F dwarf cpuid.asm \
-o cpuid.o
gcc -g -o cpuid cpuid.o
gdb session — watch the registers change
break dbg_cpuid ; after leaf-1 cpuid
run
info registers eax ebx ecx edx
print/t $ecx ; binary: bit28=AVX bit12=FMA
print/t $edx ; binary: bit25=SSE bit26=SSE2
display/t $eax ; sticky binary view
stepi ; watch the words get saved
continue
One command debugging option
make inspect PROG=cpuid
builds this program with debug info and runs its gdb script automatically — every command on the left, no typing.
System Programming Laboratory · SSE / AVX in assembly
10 / 37

## Slide 12
PROGRAM 2 · SCALAR_SSE.ASM
Scalar ops
scalar_sse.asm — three single-lane routines
section .rodata
one_f: dd 1.0
c41: dd 41.0
c3: dd 3.0
c7: dd 7.0
section .text
addone_f:
addss xmm0, [rel one_f] ; xmm0[0] += 1.0f
ret ; result stays in xmm0 (ABI)
fmax2_f:
maxss xmm0, xmm1 ; max(a, b), lane 0
ret
fsqrt_f:
sqrtss xmm0, xmm0 ; sqrt(x), lane 0
ret
Scalar = lane 0 only
addss / maxss / sqrtss each touch only lane 0 of the xmm register; the other lanes are left alone. Inputs arrive in xmm0 (and xmm1); the result stays in xmm0 — exactly the ABI.
System Programming Laboratory · SSE / AVX in assembly
11 / 37

## Slide 13
PROGRAM 2 · SCALAR_SSE.ASM — DRIVER & OUTPUT
scalar_sse.asm — main + the print helper
main:
movss xmm0, [rel c41] ; load 41.0f
call addone_f ; -> 42.0f
lea rdi, [rel s_add]
call print_f
movss xmm0, [rel c3] ; a = 3
movss xmm1, [rel c7] ; b = 7
call fmax2_f ; -> 7.0f
...
print_f:
cvtss2sd xmm0, xmm0 ; widen for %f
mov eax, 1 ; AL = 1 xmm arg
call printf wrt ..plt
output
$ ./scalar_sse
addss 41.0+1.0 = 42.000000
maxss max(3,7) = 7.000000
sqrtss sqrt(2.0) = 1.414214
The hidden conversion
Each result is a 32-bit float, but %f reads a 64-bit double. cvtss2sd does the widening the C compiler would have inserted for you.
System Programming Laboratory · SSE / AVX in assembly
12 / 37

## Slide 14
PROGRAM 2 · DEBUGGING
build with debug info (-g -F dwarf)
nasm -f elf64 -g -F dwarf \
scalar_sse.asm -o scalar_sse.o
gcc -g -o scalar_sse scalar_sse.o
gdb session — watch the registers change
break dbg_scalar ; inside addone_f
run
print $xmm0.v4_float ; {41,0,0,0}
display $xmm0.v4_float ; sticky
stepi ; run the addss
print $xmm0.v4_float ; {42,0,0,0}
break fmax2_f ; next routine
continue
info registers xmm0 xmm1
What to watch
Scalar ops touch only lane 0. The .v4_float view shows all four lanes, so you can see that addss / maxss / sqrtss change lane 0 and leave the rest untouched. display re-prints the register after every stepi, so the change is obvious.
System Programming Laboratory · SSE / AVX in assembly
13 / 37

## Slide 15
NAMING · BEYOND THE BASE PATTERN (1/2)
Fused multiply-add: reading vfmadd213ss
FMA names add ONE thing to the grammar: three digits that fix the operand order. Everything else is familiar.
v
AVX prefix
fmadd
fused multiply-add
213
operand order
ss
scalar · single
what 213 / 231 mean
; the digits name which operand is which:
; dst/op1 <- op? * op? + op?
vfmadd213ss op1, op2, op3
-> op1 = op2 * op1 + op3 ; the '213' order
vfmadd231ps op1, op2, op3
-> op1 = op2 * op3 + op1 ; the '231' order
Why FMA at all
One instruction does a multiply AND an add with a SINGLE instruction — faster, and more accurate than a separate mul then add.
System Programming Laboratory · SSE / AVX in assembly
14 / 37

## Slide 16
PROGRAM 3 · FMA_HORNER.ASM
A Taylor series for eˣ, evaluated by Horner's rule
Horner's rule
e^x ≈ a0 + x·(a1 + x·(a2 + …)). Where
Evaluate inside-out: start the accumulator at the top coefficient, then repeat acc ← x·acc + coef[i]. Each step is exactly one FMA (the 213 form from the previous slide).
System Programming Laboratory · SSE / AVX in assembly
15 / 37

## Slide 17
PROGRAM 3 · FMA_HORNER.ASM
A Taylor series for eˣ, evaluated by Horner's rule
System Programming Laboratory · SSE / AVX in assembly
15 / 37

## Slide 18
PROGRAM 3 · FMA_HORNER.ASM
Printing floating-point with xmm
System Programming Laboratory · SSE / AVX in assembly
15 / 37

## Slide 19
PROGRAM 3 · FMA_HORNER.ASM — RUN IT
FMA-Horner vs the library, side by side
shell — note the -lm
nasm -f elf64 fma_horner.asm -o fma_horner.o
gcc fma_horner.o -o fma_horner -lm ; needs libm
./fma_horner
output
x horner_fma expf
-2.0 0.135335 0.135335
-1.0 0.367879 0.367879
0.0 1.000000 1.000000
1.0 2.718282 2.718282
2.0 7.389046 7.389056
Reading the result
The two columns match to ~6 digits.
The tiny gap at x = 2.0 (…046 vs …056) is exactly the truncation error of an 11-term Taylor series — the polynomial is finite, expf is not.
System Programming Laboratory · SSE / AVX in assembly
16 / 37

## Slide 20
PROGRAM 3 · DEBUGGING
Watch the accumulator on each FMA step
build with debug info (-g -F dwarf)
nasm -f elf64 -g -F dwarf \
fma_horner.asm -o fma_horner.o
gcc -g -o fma_horner fma_horner.o -lm ; needs -lm
gdb session — watch the registers change
break dbg_fma ; the vfmadd213ss
run
print $xmm0.v4_float ; x
print $xmm1.v4_float ; acc before term
display $xmm1.v4_float ; sticky acc
stepi ; acc <- x*acc + coef[i]
continue ; next term (hits again)
continue 11 ; skip one whole polynomial
What to watch
The breakpoint sits on the FMA, so every time you continue you stop one Horner step later.
Watching xmm1 (the accumulator) lets you see the polynomial build up term by term - continue N skips N breakpoint hits — handy to jump to the next x value.
One command
make inspect PROG=fma_horner
builds this program with debug info and runs its gdb script automatically — every command on the left, no typing.
System Programming Laboratory · SSE / AVX in assembly
17 / 37

## Slide 21
SESSION 2
Packed parallelism & inspection
One instruction over many lanes — then open the debugger and read the live register every way at once.
System Programming Laboratory · SSE / AVX in assembly
18 / 37

## Slide 22
System Programming Laboratory · SSE / AVX in assembly
18 / 37

## Slide 23
PROGRAM 4 · PACKED.ASM
One instruction, every lane — the vertical operation
a
1
2
3
4
b
10
20
30
40
addps
11
22
33
44
one instruction — all four lanes at once
packed.asm — 4 lanes (xmm, 128-bit)
add4_ps:
movups xmm0, [rsi] ; load a[0..3]
addps xmm0, xmm1 ; 4 adds in parallel
movups [rdi], xmm0 ; store the 4 results
The vertical loop
addps means: for all lanes i, v[i] = a[i] + b[i]. The lanes are independent, so the hardware does them simultaneously. There is no loop around the instruction itself.
Wider = more lanes
addps over xmm does 4. The AVX form vaddps over ymm does 8 — note its 3-operand shape: vaddps ymm0, ymm0, ymm1. Same idea, double the width.
System Programming Laboratory · SSE / AVX in assembly
19 / 37

## Slide 24
PROGRAM 4 · PACKED.ASM — 8 LANES & OUTPUT
The same operation, doubled width
packed.asm — 8 lanes (ymm, 256-bit)
add8_ps:
vmovups ymm0, [rsi] ; load a[0..7]
vmovups ymm1, [rdx] ; load b[0..7]
vaddps ymm0, ymm0, ymm1 ; 8 adds at once
vmovups [rdi], ymm0
vzeroupper ; AVX hygiene before ret
ret
shell
# build & run
make packed && ./packed
output
$ ./packed
SSE: 4 lanes (xmm, 128-bit)
a : 1 2 3 4
b : 10 20 30 40
addps : 11 22 33 44
subps : -9 -18 -27 -36
mulps : 10 40 90 160
AVX: 8 lanes (ymm, 256-bit)
vaddps : 11 22 33 44
55 66 77 88
System Programming Laboratory · SSE / AVX in assembly
20 / 37

## Slide 25
PROGRAM 4 · DEBUGGING
Watch every lane update on one instruction
build with debug info (-g -F dwarf)
nasm -f elf64 -g -F dwarf packed.asm \
-o packed.o
gcc -g -o packed packed.o
gdb session — watch the registers change
break dbg_addps ; the 4-lane addps
run
print $xmm0.v4_float ; a = {1,2,3,4}
print $xmm1.v4_float ; b = {10,20,30,40}
stepi ; ONE addps -> all 4 lanes
print $xmm0.v4_float ; {11,22,33,44}
break dbg_vaddps ; the 8-lane vaddps
continue
print $ymm0.v8_float ; 8 lanes (ymm)
What to watch
The whole point of packed: a SINGLE stepi over addps changes all four lanes at once, and over vaddps all eight. Compare .v4_float on xmm (128-bit) with .v8_float on ymm (256-bit) — same operation, double the lanes.
One command
make inspect PROG=packed
builds this program with debug info and runs its gdb script automatically — every command on the left, no typing.
System Programming Laboratory · SSE / AVX in assembly
21 / 37

## Slide 26
PROGRAM 5 · DOTPROD.ASM
A reduction: packed FMA, then a cross-lane fold
Phase 1 — vertical (easy)
Sweep 8 elements per step. One vfmadd231ps does, for all 8 lanes, acc[i] += a[i]·b[i] with one rounding. After the loop, acc holds 8 partial sums — one per lane.
Phase 2 — the catch
A dot product is ONE number, but the sum is spread across 8 lanes. Combining lanes means moving data BETWEEN lanes — a point of synchronization. We do it once, at the very end.
dotprod.asm — vertical loop + fold
.loop: ; sweep 8 floats at a time
vmovups ymm1, [rdi+rax*4]
vmovups ymm2, [rsi+rax*4]
vfmadd231ps ymm0, ymm1, ymm2 ; acc += a*b
add rax, 8
jmp .loop
.reduce: ; 8 lanes -> 1
vextractf128 xmm1, ymm0, 1
vaddps xmm0, xmm0, xmm1 ; -> 4
vhaddps xmm0, xmm0, xmm0 ; -> 2
vhaddps xmm0, xmm0, xmm0 ; -> 1
System Programming Laboratory · SSE / AVX in assembly
22 / 37

## Slide 27
PROGRAM 5 · DOTPROD.ASM — THE FOLD
Eight partial sums collapse to one
8 lanes (ymm)
+ extractf128 → 4
haddps → 2
haddps → 1
Cross-lane motion happens only here — once, after the whole loop. That is what makes a reduction the interesting part of SIMD.
output — both agree
$ ./dotprod
AVX+FMA (8 lanes
+ fold) = 32762.0
scalar reference = 32762.0
The cross-check
A plain one-element-at-a-time scalar loop computes the same sum. Matching values prove the packed version and its fold are correct.
System Programming Laboratory · SSE / AVX in assembly
23 / 37

## Slide 28
PROGRAM 5 · DEBUGGING
Watch 8 partial sums, then the fold to 1
build with debug info (-g -F dwarf)
nasm -f elf64 -g -F dwarf dotprod.asm \
-o dotprod.o
gcc -g -o dotprod dotprod.o
gdb session — watch the registers change
break dbg_dot_acc ; the accumulating FMA
run
display $ymm0.v8_float ; 8 partial sums
stepi ; one FMA folds in 8 more
break dbg_dot_fold ; start of the fold
continue
print $ymm0.v8_float ; 8 partials
stepi ; watch 8 -> 4 -> 2 -> 1
print $xmm0.v4_float
What to watch
Two breakpoints tell the two-phase story. At dbg_dot_acc you see the 8 lanes accumulate. At dbg_dot_fold you step the cross-lane collapse (vextractf128, then two vhaddps) and watch the partial sums merge into a single number in lane 0.
One command
make inspect PROG=dotprod
builds this program with debug info and runs its gdb script automatically — every command on the left, no typing.
System Programming Laboratory · SSE / AVX in assembly
24 / 37

## Slide 29
PROGRAM 6 · LOADS.ASM
Aligned vs unaligned moves
loads.asm — the only difference is aps vs ups
sum_aligned:
vmovaps ymm1, [rdi+rax*4] ; FAULTS if not 32-aligned
vaddps ymm0, ymm0, ymm1
sum_unaligned:
vmovups ymm1, [rdi+rax*4] ; works at ANY address
vaddps ymm0, ymm0, ymm1
The a / u dimension
vmovaps = ALIGNED: faults unless the address is 32-byte aligned. vmovups = UNALIGNED: never faults. On aligned data both cost the same on modern CPUs.
Rule of thumb
Prefer the unaligned form unless you specifically WANT the alignment check. The program sums the same array both ways (identical result), then does a vmovups from a deliberately misaligned address (arr+1) — where vmovaps would have crashed.
System Programming Laboratory · SSE / AVX in assembly
25 / 37

## Slide 30
PROGRAM 6 · LOADS.ASM — RUN IT
Same answer; one address only one form survives
shell
make loads && ./loads
output
$ ./loads
Summing 4096 aligned floats, two ways:
vmovaps (aligned) = 4096.0
vmovups (unaligned) = 4096.0
vmovups from arr+1 -> lane0 = 1.0
What the last line proves
arr+1 float is one float past a 32-byte boundary, so it is NOT aligned. vmovups reads it anyway and lands arr[1] = 1.0 in lane 0.
Had we used vmovaps at that same address, the program would have died with a fault (SIGSEGV) instead of printing. That single contrast is the whole lesson: unaligned is the safe default.
System Programming Laboratory · SSE / AVX in assembly
26 / 37

## Slide 31
PROGRAM 6 · DEBUGGING
Watch a load fill ymm1; see the misaligned case
build with debug info (-g -F dwarf)
nasm -f elf64 -g -F dwarf loads.asm \
-o loads.o
gcc -g -o loads loads.o
gdb session — watch the registers change
break dbg_aligned ; on the vmovaps
run
print $ymm1.v8_float ; stale, before load
stepi ; ALIGNED load fills ymm1
print $ymm1.v8_float ; {1,1,1,1,1,1,1,1}
break dbg_misaligned ; vmovups from arr+1
continue
stepi ; unaligned load succeeds
print $ymm0.v8_float
What to watch
Step the vmovaps and watch ymm1 fill with eight 1.0s — a load is just data moving into the register. Then the dbg_misaligned breakpoint puts you on the vmovups from arr+1: stepping it succeeds, where a vmovaps at that unaligned address would have crashed.
One command
make inspect PROG=loads
builds this program with debug info and runs its gdb script automatically — every command on the left, no typing.
System Programming Laboratory · SSE / AVX in assembly
27 / 37

## Slide 32
NAMING · BEYOND THE BASE PATTERN (2/2)
Integer moves: reading vmovdqu
The last program loads raw integer data, so it uses an integer move. Its name follows a parallel grammar — different suffixes, same idea.
v
AVX prefix
mov
move
dq
double-quadword (128/256 bits of integer)
u
unaligned
two move families, side by side
; the float moves we already met:
vmovaps ; move · aligned · packed-single (float)
vmovups ; move · unaligned · packed-single (float)
; the integer move, for raw bits:
vmovdqu ; move · double-quad · unaligned (int)
Why an integer move here
regview loads dq 1,2,3,4 — four 64-bit integers — and treats the 256 bits as raw data, not as floats. vmovdqu is the move that says 'just the bits, please.' Same aligned/unaligned choice (vmovdqa exists too), just an integer flavour.
System Programming Laboratory · SSE / AVX in assembly
28 / 37

## Slide 33
PROGRAM 7 · REGVIEW.ASM
Load a known pattern into ymm0
regview.asm — straight from the lecture
section .data
align 32
A: dq 1, 2, 3, 4 ; four 64-bit ints
section .text
main:
vmovdqu ymm0, [rel A] ; 256 bits -> ymm0
after_load: ; <- gdb breakpoint here
vmovdqu [rel buf], ymm0 ; copy out to print
vzeroupper
Two ways to look
1. Run it — the program prints the bytes through several types.
2. Debug it — stop at after_load and read the live $ymm0 (next slides).
The after_load label
It sits immediately AFTER the load, so a breakpoint there catches ymm0 already filled. We export it (global after_load) so gdb can break on it by name.
vzeroupper before returning avoids the SSE/AVX transition penalty — good AVX hygiene.
System Programming Laboratory · SSE / AVX in assembly
29 / 37

## Slide 34
INSPECTING · THE KEY IDEA
One bit-pattern, many types — a union
A ymm register is just 256 bits. Nothing in the bits says what type they are. The same storage can be read as any of these — nothing is converted, each is a different lens.
4 × int64
{ 1, 2, 3, 4 }
8 × int32
{ 1,0, 2,0, 3,0, 4,0 }
16 × int16
{ 1,0,0,0, 2,0,0,0, … }
32 × byte
{ 01 00 00 00 … }
4 × double
{ 4.9e-324, 9.9e-324, … }
8 × float
{ 1.4e-45, 0, 2.8e-45, 0, … }
gdb shows them all for the live register; regview prints the same views from a copy of the bytes.
System Programming Laboratory · SSE / AVX in assembly
30 / 37

## Slide 35
INSPECTING · INTO THE DEBUGGER
make inspect — build with debug info, stop at the load
shell — why debug info matters
# Makefile builds regview WITH DWARF, then:
make inspect
# == gdb -q -x inspect.gdb ./regview
nasm -f elf64 -g -F dwarf regview.asm \
-o regview.o ; -g: debug info
gcc -g -o regview regview.o
core gdb commands
# inside gdb, by hand:
break after_load ; stop after load
run ; ymm0 now filled
continue ; resume
stepi ; one instruction
quit
Why break AFTER the load
The label after_load is the first instruction past vmovdqu ymm0, [rel A]. Breaking there means ymm0 already holds the pattern when we stop — no need to single-step the RIP-relative load. Building with -g -F dwarf is what lets gdb resolve the label 'after_load' by name instead of a bare address.
System Programming Laboratory · SSE / AVX in assembly
31 / 37

## Slide 36
INSPECTING · READING $YMM0 LIVE
print the register through each lens
inspect.gdb — the commands it runs
print $ymm0.v4_int64
print $ymm0.v8_int32
print $ymm0.v8_float
print $xmm0.v2_int64 ; low 128 bits
info registers ymm0 ; the whole union
; a sticky view that re-prints
; after every step:
display $ymm0.v4_int64
stepi ; watch it update
what gdb prints
Breakpoint 1, after_load ()
$1 = {1, 2, 3, 4}
(ymm0.v4_int64)
$2 = {1,0, 2,0, 3,0, 4,0}
(ymm0.v8_int32)
$3 = {1.40e-45, 0,
2.80e-45, 0, ...}
(ymm0.v8_float)
$4 = {1, 2} ; xmm0 = low half
System Programming Laboratory · SSE / AVX in assembly
32 / 37

## Slide 37
INSPECTING · MAKING SENSE OF IT
Why each view looks the way it does
v4_int64
{ 1, 2, 3, 4 }
exactly what we stored — the lens we wanted
v8_int32
{ 1,0, 2,0, 3,0, 4,0 }
each int64 splits into a low half (1..4) and a zero high half
v8_float
{ 1.4e-45, 0, 2.8e-45, … }
the SAME low halves read as float bits = tiny denormals
v4_double
{ 4.9e-324, 9.9e-324, … }
each int64 read as a double = a denormal near zero
The lesson: the bits never changed — only the type we used to read them. Choose the lens that matches your data.
System Programming Laboratory · SSE / AVX in assembly
33 / 37

## Slide 38
INSPECTING · THE PAYOFF
Program output and gdb agree — same bits, two sources
from a COPY of the bytes (the program)
$ ./regview
v4_int64 = 1 2 3 4
v8_int32 = 1 0 2 0 3 0 4 0
v8_float = 1.4e-45 0 2.8e-45 0
4.2e-45 0 5.6e-45 0
from the LIVE register (gdb)
(gdb) print $ymm0.v4_int64
$1 = {1, 2, 3, 4}
(gdb) print $ymm0.v8_int32
$2 = {1,0, 2,0, 3,0, 4,0}
(gdb) print $ymm0.v8_float
$3 = {1.40e-45, 0, 2.80e-45,...}
System Programming Laboratory · SSE / AVX in assembly
34 / 37

## Slide 39
RECAP
Seven programs, two sessions
1
cpuid.asm
detect SSE/AVX with the cpuid instruction
1
scalar_sse.asm
scalar ops · [rel] · cvtss2sd · the ABI
1
fma_horner.asm
vfmadd213ss: Taylor series by Horner
2
packed.asm
addps / vaddps — one op, every lane
2
dotprod.asm
packed FMA (231) + a cross-lane fold
2
loads.asm
aligned vs unaligned moves
2
regview.asm
vmovdqu ymm0, then inspect it in gdb
All seven are pure assembly. Read the .asm, run it, inspect the registers in gdb — that is the whole loop.
System Programming Laboratory · SSE / AVX in assembly
35 / 37

## Slide 40
REFERENCE · THE COMMANDS
Running and debugging
shell
# build & run (make)
make ; build all seven
make run ; build + run in order
make inspect ; regview under gdb
make inspect PROG=packed ; any program
# PROG = cpuid | scalar_sse |
# fma_horner | packed | dotprod |
# loads | regview
make clean ; remove binaries + .o
gdb
# gdb -- the commands you reuse
break <dbg_label> ; per-program label
run
print $xmm0.v4_float ; 4 floats
print $ymm0.v8_float ; 8 floats
print $ymm0.v4_int64 ; regview
info registers ymm0 ; every view
display $ymm0.v8_float ; sticky
print/t $ecx ; binary (cpuid)
stepi / nexti ; one instruction
continue / quit
System Programming Laboratory · SSE / AVX in assembly
36 / 37